ECE233

Laboratory Experiment 5

Ladder Network

Ladder Network: A ladder network is used in order to obtain gradually increasing voltage levels. These voltage levels demonstrate a regular structure like a ladder. The operation of the ladder network is supported and provided by the input terminal nodes. Either a constant DC voltage (VS) is applied to these nodes or they are grounded. Hence, these nodes are either activated (by applying constant voltage) or deactivated (by grounding). The number of input terminal nodes determines the number of voltage levels that will occur. If there are N input terminal nodes, the number of voltage levels that can be obtained is equal to 2N. The smallest of these voltage levels is equal to zero where as the highest of them will be equal to . Thus, the incremental change from a lower level to one higher level will be equal to .

1-) Construct the ladder network shown in Figure 1 (R1=10 kΩ, R2=5 kΩ). This ladder network has 4 input terminal nodes (A, B, C, D) and an output node (shown by node E). A voltmeter is also connected to the circuit for measuring the voltage at node E. Fill up the voltage measurements part (Voltage at node E) in Table 1 according to the different input terminal node voltage configurations. If an input terminal node is active (ON) than apply VS=16 Volt to the node. If an input terminal node is inactive (OFF) apply 0 Volt to the node (simply connect the node to the ground point).

Figure 1: Ladder network for voltage measurements.

Questions:

- For the ladder circuit in Figure 2 (R1=10 kΩ, R2=5 kΩ), show that the output voltage (voltage at node E or VE) is equal to, where VA, VB, VC and VD are the applied voltage values to corresponding nodes A, B, C and D respectively.

Figure 2: Ladder network for deriving the output voltage at node E.

Table 1: Voltage and resistance measurements over the ladder network

|  | Node D | Node C | Node B | Node A | Voltage at node E | Resistance seen from node E |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | OFF | OFF | OFF | OFF |  |  |
| 2 | OFF | OFF | OFF | ON |  |  |
| 3 | OFF | OFF | ON | OFF |  |  |
| 4 | OFF | OFF | ON | ON |  |  |
| 5 | OFF | ON | OFF | OFF |  |  |
| 6 | OFF | ON | OFF | ON |  |  |
| 7 | OFF | ON | ON | OFF |  |  |
| 8 | OFF | ON | ON | ON |  |  |
| 9 | ON | OFF | OFF | OFF |  |  |
| 10 | ON | OFF | OFF | ON |  |  |
| 11 | ON | OFF | ON | OFF |  |  |
| 12 | ON | OFF | ON | ON |  |  |
| 13 | ON | ON | OFF | OFF |  |  |
| 14 | ON | ON | OFF | ON |  |  |
| 15 | ON | ON | ON | OFF |  |  |
| 16 | ON | ON | ON | ON |  |  |

2-) Construct the ladder network shown in Figure 3 (R1=10 kΩ, R2=5 kΩ). This ladder network has 4 input terminal nodes (A, B, C, D) and an output node (shown by node E) where the ohmmeter is connected for measuring the resistance seen from node E. Fill up the resistance measurements part (Resistance seen from node E) in Table 1 according to the different input terminal connection configurations. If an input terminal node is active (ON) than leave that node open (do not connect the node to anywhere). If an input terminal node is inactive (OFF) simply connect the node to the ground point.

Figure 3: Ladder network for resistance measurements

Questions:

- For the ladder circuit in Figure 4 (R1=10 kΩ, R2=5 kΩ), show that the resistance seen from node E (RE) is equal to 5 kΩ, when A, B, C and D are OFF (connected to ground).

- For the ladder circuit in Figure 5 (R1=10 kΩ, R2=5 kΩ), show that the resistance seen from node E (RE) is equal to 25 kΩ, when A, B, C and D are ON (connected to nowhere).

- For the ladder circuit in Figure 6 (R1=10 kΩ, R2=5 kΩ), show that the resistance seen from node E (RE) is equal to 20 kΩ, when A is OFF (connected to ground) and B, C and D are ON (connected to nowhere).

Figure 4:	Figure 5:                                       Figure 6: